MG DU Logic Board Main Connector

Function Pin

CANH	A3
CANL	A4

FORWARD DIRECTION	B3
REVERSE DIRECTION	B4

BRAKE INPUT	C3

MOTOR TEMP SENSE 1	F3
MOTOR TEMP SENSE 2	F4

SINB	G3
SINA	G4

COSB	H3
COSA	H4

ACCEL +5V	J1
ACCEL SIGNAL A	J2
ACCEL SIGNAL B	J3
ACCEL GND	J4

START SIGNAL	K4

EXCA	L3
EXCB	L4

+12V SUPPLY	M3
MAIN GROUND	M4